# MI52 - Final
1h30. Document : One sheet of paper note only. You can answer in French or English.
## Memory and OS general questions
###### A program use a pointer to a memory mapped register to access a peripheral register :
volatile unsigned int * memory_mapped_reg = (volatile unsigned int *) PHYSICAL_BASE_ADRESS + 0x8;
###### what can be the problem if the program run on an architecture with a memory cache and try to read the peripheral register ?
###### How is it resolved by cache memory controller systems.
###### Explain briefly what does a MMU (with no TLB) do when a microprocessor fetch a new data in memory i.e. what happen when a virtual memory address is generated on the microprocessor bus.
###### Explain briefly why a NAND flash without a NAND memory controller can not be used to store directly executable code ?
## Signal processing with FreeRTOS
An application on a STM32 SoC do process an analog signal : every n us, the application must get a new data from an analog to digital converter (ADC), filter the new data (signal processing algorithm) and send the calculate output on a digital to analog converter (DAC).

To sample the input data (and also send the output data) a timer interrupt is used (TIM3). The hardware and software is initialized so that every n us the interrupt service routine (ISR) of the timer is called TIM3_ISR().

We do not want the calculus of the output data to be done in the ISR as it is a very long process. The calculus will be done in a high priority task synchronized with the ISR (vTask_data_processing). The ISR will only get a new datum from the ADC and send the previous calculated datum output to the DAC.

Some functions that you can use are already written :
- uint32_t adc_get_data(void) : get a new data form the ADC
- void dac_output_data(uint32_t data) : sent the data on the analog line
- uint32_t ts_process_output_data(int data) : process the filtering of the data

The synchronisation between ISR and Task will be done through a binary semaphore. Here are the functions from the freeRTOS api that can be used :

SemaphoreHandle_t xSemaphoreCreateBinary( void );
xSemaphoreTake( SemaphoreHandle_t xSemaphore, TickType_t xTicksToWait );
xSemaphoreGive( SemaphoreHandle_t xSemaphore );
xSemaphoreGiveFromISR (SemaphoreHandle_t xSemaphore, signed BaseType_t *pxHigherPriorityTaskWoken)

Uncomplete code for the ISR and the data processing task :

SemaphoreHandle_t sem; /* The semaphore is created in the 'empty' state */

static void TIM3_ISR( void )
{
static signed BaseType_t xHigherPriorityTaskWoken;

xHigherPriorityTaskWoken = pdFALSE;

/* test the interrupt and acknowledge it */
 if (TIM3->SR & TIM_SR_UIF){
TIM3->SR = 0;

1
[...]

}
 portEND_SWITCHING_ISR( xHigherPriorityTaskWoken );
}

void vTask_data_processing( void *pvParameters )
{
sem = xSemaphoreCreateBinary();

(...)

NVIC_SetPriority ( TIM3_IRQn, 4);
NVIC_EnableIRQ (TIM3_IRQn);

for( ;; ) {

2
[...]

}
vTaskDelete( NULL );
}

Work :
###### Explain why the data processing is not done in the ISR but in a task
###### Explain what is the role of the instruction “portEND_SWITCHING_ISR( xHigherPriorityTaskWoken );” at the end of the isr
###### Complete the code of the ISR and task (1 and 2). Don't forget to comment your code and give explanations.
## Device and Driver in the driver model of linux
here is the code of a driver initialisation for a platform driver on a ARM SoC that use the device tree. The devices that use this driver are connected to a platform bus that is a generic bus.

static const struct of_device_id my_of_match[] = {
{ .compatible = "my,example", },
{ },
};
MODULE_DEVICE_TABLE(of, my_of_match);

static struct platform_driver platform_driver_example = {
.driver = {
.name = "platform_driver_example",
.owner = THIS_MODULE,
.of_match_table = my_of_match,
},
.probe = platform_driver_example_probe,
.remove = platform_driver_example_remove,
};
/* init, exit functions */
module_platform_driver(platform_driver_example);

###### When are the probe and remove function of the driver called ?
###### What is the utility of “ match table ” ?